## Slide 1: Automotive Protocols
Protocols = communication rules

## Slide 2: CAN Protocol
Developed by Bosch
Used for communication between ECUs in a vehicle
Key Features :
Multi-master communication → Any ECU can send data
Real-time communication → Fast response for important data
Error detection → Identifies and handles communication errors
High reliability → Safe and reliable for critical systems

## Slide 3: CAN Bus
CAN Bus is a network that connects all ECUs in a vehicle
It uses 2 wires: CAN High and CAN Low
It allows ECUs to share data with each other
It provides reliable communication

## Slide 4: CAN Message
CAN message is the data sent on the CAN network
It contains ID and actual data
All ECUs can read the message
Important messages are given higher priority
Types of CAN Messages :
Data Frame – used to send actual data
Remote Frame – used to request data
Error Frame – shows communication error
Overload Frame – adds delay if needed

## Slide 5: CAN Data Frame
Data frame is the most common CAN message used to send real data between ECUs
It has these main parts:
Arbitration Field – decides priority of message
Data Field – contains actual data (0 to 8 bytes)
CRC Field – checks for errors
Acknowledgement – receiver confirms message received
If no acknowledgement is received, message is sent again

## Slide 6: Arbitration Process
Multiple ECUs can send messages at the same time
Each message has an Identifier (ID)
Lower ID = Higher priority
The message with highest priority continues
Other ECUs stop and try again later
This avoids collision and ensures smooth communication

## Slide 7: CAN FD
CAN FD is the advanced version of CAN
It is faster than CAN
It can send more data in one message
It is used in modern vehicles

## Slide 8: LIN Protocol
LIN is a simple and low-cost communication protocol
It uses 1 master and multiple slave nodes
Works on single wire + ground
Speed: 1 kbps to 20 kbps (slow)
Used in windows, mirrors, seats
Supports simple data communication
Maximum wire length is about 40 meters
Less reliable than CAN, but easy to use and low cost

## Slide 9: LIN Frame Types
Unconditional → Normal communication
Event-Triggered → Sent when data changes
Sporadic → Sent by master when needed
Diagnostic → Used for fault checking
User-Defined → Custom frame
Reserved → For future use

## Slide 10: CAN vs LIN
Feature | CAN (Controller Area Network) | LIN (Local Interconnect Network)
Speed | Fast (up to 1 Mbps) | Slow (up to 20 kbps)
Cost | Higher | Low cost
Complexity | Complex system | Simple system
Communication | Multi-master | One master, multiple slaves
Wires | Two wires (CAN High, CAN Low) | Single wire + ground
Use | Engine, braking systems | Windows, mirrors, seats
Reliability | High | Lower than CAN
Data Handling | Handles critical data | Handles simple data

## Slide 11: Automotive Ethernet
Very high speed network
Used in ADAS systems
Supports cameras & sensors
Acts as backbone network

## Slide 12: Tools: CANoe & CANalyzer
Used for testing and analyzing CAN communication
Widely used in the automotive industry
CANalyzer :
Used to capture and analyze CAN messages
Helps monitor real-time communication
Used for debugging issues
CANoe :
Used for simulation and testing of ECUs
Supports network simulation and diagnostics
Helps in validation of complete system

## Slide 13: UDS (Diagnostics)
Unified Diagnostic Services
Used to detect vehicle issues
Supports firmware update
Used by service engineers

## Slide 16: UDS Message structure

## Slide 17: Automotive Networking
Connects all ECUs
Allows data flow
Uses CAN, LIN, Ethernet
Ensures proper vehicle operation

## Slide 18: Network Topologies (Connection Types)
Point-to-Point → One device connected to one device
Bus / Multi-drop → Multiple ECUs connected on same line (e.g., CAN)
Ring → ECUs connected in circular form
Star → All ECUs connected to a central unit

## Slide 19: Types of Data in Vehicle Network
Control Data → Engine, transmission, motor control
Safety / Time-Critical Data → Airbag, braking, ADAS (very fast response required)
Infotainment Data → Audio, video, navigation
Backbone Data → Connects different vehicle networks
Low-Speed Data → Doors, windows, seat control

## Slide 20: Vehicle Network Application
Safety / Time-Critical Data → Requires high speed and fast response → Example: Airbag, braking (ADAS systems)
Control Data → Used for controlling sensors and actuators → Example: Engine, transmission systems
Backbone Data → Transfers data between different networks → Used in gateway communication
Infotainment Data → Audio, video and navigation data → Requires high bandwidth (> 25 Mbps)
Multi Giga Data → Very high-speed data for advanced systems → Used in autonomous driving (ADAS, cameras)
Low Cost / Speed Data → Low-speed simple communication → Example: Door locks, window control

## Slide 21: Stellantis Architecture
Uses Domain Controllers (group of ECUs for each function)
Uses Gateway ECU to connect all networks
Communication via CAN / CAN FD
Uses Ethernet Backbone for high-speed data
Moving towards Centralized Computing

## Slide 22: Thank You